6-1	Bridge Application Program Interface


	Bridge Application Program Interface	6-1


6-1	Bridge Application Program Interface
Application Compatibility Levels

	Bridge Application Program Interface	6-1
BAPI Specification

6-1	Bridge Application Program Interface
BAPI Specification

	Bridge Application Program Interface	6-1
BAPI Specification

6-1	Bridge Application Program Interface
BAPI Specification

	Bridge Application Program Interface	6-1
BAPI Specification


Chapter 6
Bridge Application Program Interface

.i(.Bridge Application Program Interface (BAPI);
.i.BAPI.  #See Bridge Application Program Interface (BAPI);
This chapter provides application developers with an overview of the Bridge 
Application Program Interface (BAPI).  It contains the following information:

n	Introduction to BAPI

n	Application compatibility levels

n	Description of functions provided by BAPI

Introduction

BAPI allows application programs to use the communication facilities of.i.3Com 
TCP.  See also TCP protocol:BAPI;
 3Com TCP with Demand Protocol Architecture.  Software for personal computers 
can be developed to perform terminal emulation, .i.file transfer:BAPI;
.i.terminal emulation, BAPI;
file transfer, and other applications.  BAPI is designed for flexibility, 
allowing the application developer to choose the level of control over 
communications and making the details of LAN communications transparent.  In 
addition, the application developer need not be concerned with changes to the 
underlying communication mechanism, because the interface remains the same.

BAPI is a set of functions that are accessed using .i.Interrupt 14H;
Interrupt 14H.  These functions include external and .i.internal session 
management, BAPI;
.i.session management, BAPI:external;
.i.session management, BAPI:internal;
.i.external session management, BAPI;
internal session management and data transfer.

Internal session management functions allow an application control of all 
aspects of communications, including session establishment, session 
termination, and session characteristics.  Data-transfer functions provide the 
application software with the mechanism to transmit or receive data over an 
established session.

Application developers can use the internal session management functions of 
BAPI, but this is not required. .i.data :transfer functions, BAPI;
 Data-transfer functions also allow applications to use the 3Com TCP with 
Demand Protocol Architecture external session management services.

3Com TCP with Demand Protocol Architecture provides an external session 
management command interface.  Applications such as terminal emulators capable 
of direct communications (for example, displaying data via the personal 
computer monitor and accepting keyboard data) are the applications best suited 
to take advantage of external session management.  External session management 
provides an interface that accepts user .i(.commands, BAPI;
commands (for example, CONNECT and DISCONNECT).  A special key sequence or an 
.i.Enter Command Mode (ECM) character;
Enter Command Mode (ECM) character activates the command interface.  Table 6-1 
summarizes the available commands.



.i.Bridge Application Program Interface (BAPI):commands;
Table 6-1.  Command Summary

Command	Definition


CONNECT<hostname>	Execute this command when in Command mode to establish 
single or multiple connections.
SHOW SESSION	Execute this command when in Command mode to display all active 
sessions.
RESUME [<session id>]	Execute this command when in Command mode to resume the 
current session or a specified session if more than one session is active.
DISCONNECT [<session number>]	Execute this command when in Command mode to 
disconnect a specified session.  If no session is specified, it  disconnects 
the current session.
MODIFY [<session>]	Execute this command when in Command mode to modify the 
configuration of the current or specified session.


Application Compatibility Levels

BAPI augments and replaces the .i.Interrupt 14H;
.i.EtherTerm Interrupt 14H programmable interface;
EtherTerm Interrupt 14H programmable interface.  
To take advantage of the speed of the new read-and-write block functions, or to 
use the internal session management function, convert applications to use the 
new interface specification.  The interface levels and functions used by the 
application are shown in Table 6-2. 
.i.Bridge Application Program Interface (BAPI):application compatibility 
levels;

Table 6-2.  Application Compatibility Levels

Level	Function	Definition


1	A2h B AFh, B0h B B3h	External session management: the application is not 
required to handle session management.
2	A0h B AFh, B3h	Internal session management: session management is 
handled by the application.


External Session Management

.i.Bridge Application Program Interface (BAPI):external session management;
.i.external session management, BAPI;
.i.session management, BAPI:external;
Assume that application(1) and application(2) are using the external session 
management for session handling.  All function calls by an application should 
set the Session ID field of each function to zero. BAPI presents a .i.commands, 
BAPI;
command interface where characters are interpreted as commands until a 
successful completion of a .i.CONNECT command;
.i.RESUME command;
CONNECT or RESUME command.  Following a successful CONNECT or RESUME command, 
data is passed transparently through the active session.  Users can type the 
.i.Enter Command Mode (ECM) character;
Enter Command Mode (ECM) character at any time to return to the command 
interface, and then issue session management commands.


Users can have multiple applications, each with active sessions.  Users can 
have terminate-and-stay-resident applications, or they can invoke 
application(1), reenter .i.DOS:reentering from BAPI;
DOS, and then invoke application(2).  Each session opened by an application is 
available to other applications.  All sessions remain active until disconnected 
or timed out by the host.

External session management should not be used in more than one window of a 
window-management program such, as .i.DESQView;
.i.Microsoft Windows;
DESQView3 or Microsoft1 Windows1..i.windows;

Internal Session Management

.i.Bridge Application Program Interface (BAPI):internal session management;
.i.internal session management, BAPI;
.i.session management, BAPI:internal;
It is assumed that application(1) and application(2) are programs capable of 
session management.

The application must provide the user interface necessary to connect, 
disconnect, show sessions, and resume sessions.  The application must maintain 
a record of session numbers and must use the Session ID field of each function.  
It performs connections and disconnections through functions A0h and A1h.  Use 
the other functions to transmit and receive data. 

Users can invoke multiple applications, each with active sessions.  Users can 
have terminate-and-stay-resident applications, or they can invoke 
application(1), reenter DOS, and invoke application(2).  Since the applications 
are managing session information, each session opened by an application is 
available only to that application.  All sessions remain active until 
disconnected or timed out by the host.  A terminate-and-stay-resident 
application can safely terminate and stay resident without losing its sessions 
and session numbers.  When terminating without staying resident, every 
application should disconnect all active sessions, since all record of these 
sessions is lost.


BAPI Specification

.i.Bridge Application Program Interface (BAPI):specification;
This section lists and describes the functions provided by BAPI.
.i.Bridge Application Program Interface (BAPI):functions;


Table 6-3.  Functions

Function	Definition	


A0h	Connect to port 
A1h	Disconnect
A2h	Write one character
A3h	Read one character
A4h	Write one block 
A5h	Read one block 
A6h	Generate break signal
A7h	Read status
AAh B AEh	Reserved
AFh 	Interface version
B0h	Enable/disable ECM
B1h 	Enter command mode (if TE wants to trap the 
ECM character)
B2h	Get ECM watch state
B3h	Set/get configuration information


.i.Enter Command Mode (ECM) character;
The Session ID and Error parameters are added to improve information transfer 
between the application and BAPI.  Table 6-4 lists the values for the Session 
ID parameters.  Table 6-5 lists the values for Error parameters.
.i.Bridge Application Program Interface (BAPI):session ID parameter values;

Table 6-4.  Session ID Parameter Values

Value	Description	


00h	External Session Management 
01	Session 1 
02	Session 2 
nn	Session n, nn < FFh 



.i.Bridge Application Program Interface (BAPI):error parameter values;
Table 6-5.  Error Parameter Values

Value	Description	


00h 	Success
01	No characters written 
02	No characters read
03	No such session 
04	Clearinghouse name not found
05	No response from host 
06	No more sessions available
07	Session aborted 
08	Invalid clearinghouse name
09	Not supported 
10	Internal (general) network error
11	Out of memory 
12	Invalid IP address 


A detailed description of the extended functions follows:

A0h: Connect to port 

On entry	AH = A0h 
	ES:BX = <pointer to port name or address string> 
	CX = <length of host name or address string>

On exit 	AH = <error> (0, 4, 5, 6, 8, 10, 11, 12) 
	CL = <session id>

A1h: Disconnect

On entry	AH = A1h 
	DH = <session id>

On exit 	AH = <error> (0, 3, 7, 10, 11) 
	BX = <unchanged> 
	DX = <unchanged>


A2h: Write one character

On entry	AH = A2h 
	AL = <character to write> 
	DH = <session id>

On exit	AH = <error> (0, 1, 3, 7, 10, 11) 
	AL = <unchanged> 
	DX = <unchanged>

A3h: Read one character

On entry	AH = A3h 
	DH = <session id>

On exit	AH = <error> (0, 2, 3, 7, 10, 11) 
	AL = <character read> (0 if no character) 
	DX = <unchanged>

A4h: Write one block

On entry	AH = A4h 
	ES:BX = <pointer to block of characters> 
	CX = <number of characters in block> 
	DH = <session id>

On exit 	AH = <error> (0, 1, 3, 7, 10, 11) 
	ES:BX = <unchanged> 
	CX = <number of characters written> 
	DX = <unchanged>

A5h: Read one block

The application provides a buffer to store received characters.

On entry	AH = A5h 
	ES:BX = <pointer to block of characters> 
	CX = <maximum number of characters to read> 
	DH = <session id>

On exit	AH = <error> (0, 2, 3, 7, 10, 11) 
	ES:BX = <unchanged> 
	CX = <number of characters read> 
	DX = <unchanged>


A6h: Generate break signal

Generates a short break signal and waits for the host to turn on data delivery, 
if it was turned off by the break.

On entry	AH = A6h 
	DH = <session id>

On exit	AH = <error> (0, 3, 7, 10, 11) 
	DH = <unchanged>

A7h: Read status

On entry	AH = A7h 
	DH = <session id>

On exit	AH = <error> (0, 3, 7, 10, 11) 
	CX = <number of characters waiting to be read> 
	DX = <unchanged>

AFh: Interface version

The previous version of this interface and IBM BIOS return from this function 
with AX unknown, which helps applications determine whether to use the new or 
old functions.  The application should check for a return of AX = AF01h.

On entry	AH = AFh 
	AL = 00h
	BX = AAAAh (undefined in previous application)

On exit	AH = AFh 
	AL = 01h (version of this interface)
	If BX = AAAAh on entry, then
		BH = <protocol type> (01 for 3Com TCP/IP)
		BL = <version> (current version for this protocol type)
	else BX = unchanged

B0h: Enable/disable ECM

.i.Enter Command Mode (ECM) character;

A switch on the command line changes the ECM character.  It cannot be a 
character sequence.  If the application requires a key sequence, disable the 
ECM, intercept the sequence, and invoke function B1h.  If the application 
transmits characters that include 
the ECM (for example, binary file transfer), disable the ECM character.

On entry	AH = B0h 
	AL = <flag> (1 enable, 0 disable)

On exit	AH = <error> (0, 7, 10)

B1h: Enter command mode

.i.Enter Command Mode (ECM) character;
This function is provided for TEs who need to trap the ECM character.

On entry	AH = B1h

On exit 	AH = <error> (0, 7, 10) 
	All other registers unchanged.

B2h: Get ECM watch state

On entry	AH = B2h

On exit	AH = <error> (0, 7, 10)
	AL = <flag> (1 = enabled, 0 = disabled)

B3h: Set/get configuration information

On entry	AH = B3h
	AL = <flag> (1 = set, 0 = get)
	DH = <session id>
	DL = <config item number> (0 = End-of-line mapping)
	CX = <config item value>
		(if AL = 1 and DL=0) 

		CH = Application End-of-line value (application to Telnet client)
		1 = Application will send a single CR
		2 = Application will send a (CR, ?) pair

		CL = Driver End-of-line value (Telnet client to Telnet server)
		1 = Driver should send a (CR, NUL) pair
		2 = Driver should send a (CR, LF) pair

On exit	AH = <error> (0, 3, 9, 10, 11)
	if operation was "get" (AL = 0),
	CX = <config item value>
		(see definition of CH and CL above)
	All other registers unchanged..i).Bridge Application Program Interface 
(BAPI);