Release 10.1 of the Crynwr 3C509 Packet Driver

For the copyright, see COPYING.DOC.  In part it says that: Anyone
with a copy of the drivers may give it away, and the source code for
all modules must be available.

NO WARRANTY, see COPYING.DOC, but support for packet drivers is
available, see SUPPORT.DOC.

This release contains only the 3C509 packet driver.  Many more packet
drivers (including 3c501, 3c503, 3c505, 3c507, and 3c523) are
available in the complete packet driver release.  See HOWTOGET.IT for
availability.


Installation:

The packet driver has two parameters, one required and one optional.

Run the driver with one parameter, the software interrupt. A packet
driver needs to have a software interrupt assigned to it for other
programs to access it.  I recommend 0x7f or 0x7e.

The driver needs an initial ID port to access the 3C509 hardware. The
driver uses a default of 0x110 for the ID port.  If you have a
conflict at port 0x110 (very few machines do), the packet driver will
be unable to initialize the adapter, so try specifying a different
value as the second parameter.  ID port must be 0x100, 0x110, 0x120,
..., 0x1f0.


Notes:

The 3C509 is a good, fast, cheap board.  However, it requires close
cooperation between the driver and the adapter.  If your system has
high interrupt latency, this cooperation is disrupted.  Also, the
decisions made by different driver authors will affect whether a
driver/adapter combination will work in your system.

In particular, the bursty high packet rate typical of NFS
implementations causes the 3C509 to overrun.  You may have to reduce
the maximum length of packets sent to the 3C509 to transfer large
files.

This driver is ONLY supported and tested on the 3C509.  This driver
will be enhanced in the future to support the EISA-3C579 and MC-3C529
versions of the Etherlink III  family.  It currently contains code to
also support the EISA-3C579 card.  I have only been able to test
the driver on my EISA 486, where it doesn't work.  The problem shows
itself by corrupting the contents of packets.  But this could just be
my system (which is of dubious origin).  If you would like to beta
test this driver on a 3C579, please tell me how your trial went.

Please report problems.  I cannot guarantee that I will work on your
problem if you are not a Crynwr customer.  I CAN guarantee that I
will not work on it if you don't report it to me.  Written reports
are preferred to phone calls.

Russell Nelson
nelson@crynwr.com
315-268-1925 voice
315-268-9201 FAX
Crynwr Software, 11 Grant St., Potsdam, NY 13676