User documentation for the packet driver collection
                                   Russell Nelson
                                 Clarkson University
                                  Potsdam, NY 13676
                              nelson@clutx.clarkson.edu


          Why?

               Every PC Ethernet board is different.  The 3c501 was, for
          some time, the most popular board, and would have become the
          defacto standard but for its poor performance.  By the time 3Com
          created a board with acceptable performance, so had many others,
          and 3Com lost its lead.  FTP Software, in order to support each
          of these boards without losing its collective mind, created the
          Packet Driver Spec (PDS).


          What?

               Some boards use DMA, some use programmed I/O, and some use
          shared memory.  The PDS masks the differences between these
          boards by defining a software interface to the boards.  This
          software interface is a software interrupt in the range between
          0x60 (hex) and 0x80.


          How?

               The packet driver must be installed prior to use.  Since
          each packet driver takes only 1800 bytes, this is best done in
          your autoexec.bat.  Since the Ethernet boards typically have
          jumpers on board, the packet driver must be informed of the
          values of these jumpers (auto-configure is possible, but can
          disturb other boards).  The first parameter is the software in-
          terrupt used to communicate with the packet driver.  And again,
          because each board is different, the rest of the parameters will
          be different.

          Before installing the packet driver, you must choose a software
          interrupt number in the range between 0x60 and 0x80.  Some of
          these interrupts are used for other purposes, so your first
          choice may not work.  See Appendix A for the section of Ralf
          Brown's interrupt list between 0x60 and 0x80.

          Running a packet driver with no specifications will give a usage
          message.  The parameters for each packet driver are documented
          below.







          3C501

               usage: 3C501 <packet_int_no> <int_no> <io_addr>

               The 3c501 requires two additional parameters -- the
          hardware interrupt number and the I/O address.  The defaults are
          3 and 0x300.


          3C503

               usage: 3C503 <packet_int_no> <int_level(2-5)> <io_addr>

               The 3c503 requires two additional parameters -- the
          hardware interrupt number and the I/O address.  The defaults are
          2 and 0x300.  The 3c503 uses shared memory whose address is set
          by jumpers, but the software can ask the board what the address
          is.



          3c523

               usage: 3c523 <packet_int_no> <int_no> <io_addr> <base_addr>

               The 3c523 requires three additional parameters -- the
          hardware interrupt number, the I/O address, and the memory base
          address.  The defaults are 3 and 0x300 and 0xc000.



          NI5010

               usage: NI5010 <packet_int_no> <int_no> <io_addr>

               The NI5010 requires two additional parameters -- the
          hardware interrupt number and the I/O address.  The defaults are
          3 and 0x300.



          NI5210

               usage: ni5210 <packet_int_no> <int_no> <io_addr> <base_addr>

               The NI5210 requires three additional parameters -- the
          hardware interrupt number, the I/O address, and the memory base
          address.  The defaults are 2 and 0x360 and 0xd000.  Note that In-
          terlan sets the default memory base to 0xa000, which is
          brain-damaged, because that area of memory is specifically
          reserved for video adapters, and in fact the EGA and VGA use it.







          SLIP8250

               usage: SLIP8250 packet_int_no [driver_class] [int_no]
                  [io_addr] [baud_rate] [send_buf_size] [recv_buf_size]
                  The driver_class should be SLIP, KISS, AX.25, or a
                  number.

               The SLIP8250 is not strictly an Ethernet adapter, however
          some software packages (such as KA9Q's NET) support Serial Line
          IP (SLIP).  SLIP must be specially supported because it doesn't
          use ARP and has no hardware addresses prepended to its packets.
          The PDS is not clear on this, but the packet driver does the SLIP
          encoding.

          The parameters are as follows.  The driver_class is the class
          that is returned to a client of the packet driver spec in the
          Drive_Info call.  The int_no is the hardware interrupt number,
          defaults to 3 (COM1).  The io_addr is the hardware I/O address,
          defaults to 0x3f8 (COM1).  The baud_rate defaults to 4800 baud.
          The send_buf_size and recv_buf_size default to 3000 each.


          WD8003E

               usage: WD8003E <packet_int_no> <int_level> <io_addr>
          <mem_base>

               The WD8003E requires three additional parameters -- the
          hardware interrupt number, the I/O address, and the memory base
          address.  The defaults are 2 and 0x280 and 0xc400.


          Who?

          See the file support.txt for a listing of all the people who
          contributed packet drivers.







                                     Appendix A
                   Interrupt usage in the range 0x60 through 0x80



          60 -- -- reserved for user interrupt
          60 -- -- FTP Driver - PC/TCP Packet Driver Specification
          60 01 FF FTP Driver - DRIVER INFO
          60 02 -- FTP Driver - ACCESS TYPE
          60 03 -- FTP Driver - RELEASE TYPE
          60 04 -- FTP Driver - SEND PACKET
          60 05 -- FTP Driver - TERMINATE DRIVER FOR HANDLE
          60 06 -- FTP Driver - GET ADDRESS
          60 07 -- FTP Driver - RESET INTERFACE
          60 11 -- 10-NET - LOCK AND WAIT
          60 12 -- 10-NET - LOCK
          60 13 -- 10-NET - UNLOCK
          60 20 -- FTP Driver - SET RECEIVE MODE
          60 21 -- FTP Driver - GET RECEIVE MODE
          60 24 -- FTP Driver - GET STATISTICS
          61 -- -- reserved for user interrupt
          62 -- -- reserved for user interrupt
          63 -- -- reserved for user interrupt
          64 -- -- reserved for user interrupt
          65 -- -- reserved for user interrupt
          66 -- -- reserved for user interrupt
          67 -- -- LIM EMS
                   ...
          67 DE 00 Virtual Control Program Interface - INSTALLATION CHECK
                   ...
          68 01 -- APPC/PC
                   ...
          69 -- -- unused
          6A -- -- unused
          6B -- -- unused
          6C -- -- system resume vector (CONVERTIBLE)
          6C -- -- DOS 3.2 Realtime Clock update
          6D -- -- VGA - internal
          6E -- -- unused
          6F -- -- Novell NetWare - PCOX API (3270 PC terminal interface)
          6F 00 -- 10-NET - LOGIN
                   ...
          70 -- -- IRQ8 - AT/XT286/PS50+ - REAL-TIME CLOCK
          71 -- -- IRQ9 - AT/XT286/PS50+ - LAN ADAPTER 1
          72 -- -- IRQ10 - AT/XT286/PS50+ - RESERVED
          73 -- -- IRQ11 - AT/XT286/PS50+ - RESERVED
          74 -- -- IRQ12 - PS50+ - MOUSE INTERRUPT
          75 -- -- IRQ13 - AT/XT286/PS50+ - 80287 ERROR
          76 -- -- IRQ14 - AT/XT286/PS50+ - FIXED DISK
          77 -- -- IRQ15 - AT/XT286/PS50+ - RESERVED
          78 -- -- not used
          79 -- -- not used
          7A -- -- Novell NetWare - LOW-LEVEL API
          7A -- -- AutoCAD Device Interface
          7B -- -- not used







          7C -- -- not used
          7D -- -- not used

          7E -- -- not used
          7F -- -- HDILOAD.EXE - 8514/A VIDEO CONTROLLER INTERFACE
          7F -- -- HLLAPI (High-Level Language API)
          80 -- -- reserved for BASIC